Rock Solid ™ Gibraltar post replacement instructions

Please read completely before proceeding

- After you have removed the bridge, check if the Rock Solid posts will easily fit in the bridge post holes. DO NOT force them or the threads may be damaged. Gibraltar’s are made from pot metal and after time the hole the post sits in will deform on the bottom side of the bridge where it contacts the posts and become smaller. A little cleanup with a needle file may be required to remove the deformed metal at the bottom of the hole and allow the post to enter.

- Eyeball the original post heights before removing to help place the Rock Solid posts at appx the correct height.

- Screw the posts into the sustain block or inserts to make sure they move freely. If not we recommend adding a few drops, very little is required, of a light machine oil to the large post threads before inserting. The Rock Solid post threads are slightly oversize to make better contact and occasionally there will be rubbing compound, dirt and other debris in the sustain block or insert threads that make screwing the post in a little tight. The lubricant helps clear all that out. Use the post tool to run them up and down if necessary.

- Replace the bridge on your new posts and you should already see a dramatic reduction in front to back movement even without the lock nuts.

- We think you will find that using the bridge post tool to adjust the bridge height is much easier then using a screwdriver especially if the strings are under tension.

- Once the bridge is at the desired height, insert the bridge post tool to prevent the posts from rotating and lock down the nuts.

- If further adjustments are required, loosen the lock nuts and fine tune using the bridge post tool. If you should happen to misplace the tool you can order another or use a 1/16” or 1.5mm Allen wrench.

Any questions or comments please contact us at repropart@comcast.net